## Slide 1: Installation of a Pride of the Farm WPO12E Electric Heated Open Trough Waterer

## Slide 2: Select a pad size that an animal can comfortably stand on. This pad will be a two level 12’ x12’ monolithic pour using 2” x 6” lumber Riser tube is a 10” PVC tube – a minimum of an 8” is recommended

## Slide 3
Use crushed rock to level pad site
To reinforce concrete pad we will use wire mesh

## Slide 4
Top level of pad is sized to have 10” – 12” around the footprint of the waterer

## Slide 5
Finish the concrete pour with a rough broom finish

## Slide 6
Add crushed rock around the perimeter of pad

## Slide 7
Cut off riser tube ½” to 2” above the slab
This will prevent water and debris falling back down into riser
Important to keep riser open and free of debris

## Slide 8
Shorten grounding rod and attach ground wire from electric service to rod with clamp
Service line should be ground fault protected at the breaker box

## Slide 9
This installation used PEX pipe and a brass shut off valve
Mount outdoor waterproof electrical box on the inside of waterer cavity using four #12 – 3/4” wood screws
HINT: Mount electrical box on right hand side of cavity if left-handed to make plugging in heater and heat tape easier
Use provided 4” pipe insulation on upper portion of supply line. If riser tube is deeper than 3 feet, install additional insulation on lower portion of waterline

## Slide 10
Cut a 45* bevel at the top of 3”pipe to allow more room to remove and insert the power cord of heater
Make sure lower part of cut is still higher than top of waterer trough to prevent water falling into riser tube
INSTALLATION HACK

## Slide 11: ATTENTION: TW is consulting with ISU to check on validity of grounding
Ground wire is continued from grounding rod, up thru 3” water assembly pipe and wrapped at the base of the tube in the water to assure proper grounding in the event of stray voltage.

## Slide 12
Waterer should be mounted and sealed to concrete using provided weatherstripping or silicone caulk
Access door should be orientated to the east or south to avoid cold winter winds
Check for water leaks
Secure pipe insulation with zip ties